## Slide 1: GAMOS SIMULATIONS
By Amina Patel

## Slide 2: Contents
Description Of Simulations:
Geometry
Application of Filters (selection of events)
Results/Comparison

## Slide 3: Simulations-Geometry
Isotropic point source (141,364,662 and 1332 keV gamma rays) located 3cm from face of scatter detector
Silicon Scatter detector of varying thicknesses [100,300,750,1000 (um)]
Attached to back of scatter detector Indium layer (20um) and Silicon Asic (120um)
detector
source
3cm
z
x
Y

## Slide 4: Simulation Overview
Gamma ray enters detector interacts via compton effect. Compton electron produced, deposits its energy
Select only the Compton electrons that are produced by gamma rays from their first interaction (Compton) and deposit their energy in the detector. i.e do not travel out of the detector or are created outside detector region and travel into the detector region.

## Slide 5: Simulation Method
1.Apply “process filter” to detector region - only Compton electrons created in detector
2. Apply “Track ID filter” only electrons with Track ID 2 are selected
3. Apply Traverse Particle filter – particles neither enter or exit detector region i.e particles that are only created and stop within detector are selected
1=Gamma
2= Electron

## Slide 6: Results Summary
 | Si detector Thickness (um) | GAMOS | GEANT4
141 kev | 100 | 690 | 505
 | 300 | 1993 | 1604
 | 750 | 4937 | 4096
 | 1000 | 6506 | 5337
364 keV |  |  | 
 | 100 | 483 | 175
 | 300 | 1472 | 881
 | 750 | 3693 | 2718
 | 1000 | 4937 | 3467
662 keV |  |  | 
 | 100 | 206 | 82
 | 300 | 810 | 357
 | 750 | 2531 | 1458
 | 1000 | 3495 | 2257
1332 keV |  |  | 
 | 100 | 60 | 35
 | 300 | 305 | 123
 | 750 | 1122 | 536
 | 1000 | 1671 | 768

## Slide 7: Results -141 keV
Chart: Incident gamma ray energy of 141 keV
| 100.0 | 300.0 | 750.0 | 1000.0
GAMOS | 690 | 1993 | 4937 | 6506
GEANT-4 | 505 | 1604 | 4096 | 5337

## Slide 8: Results-1332 keV
Chart: Incident gamma ray energy of 1332 keV
| 100.0 | 300.0 | 750.0 | 1000.0
GAMOS | 60 | 305 | 1122 | 1671
GEANT-4 | 35 | 123 | 536 | 768

## Slide 9: Conclusion
GEANT4 and GAMOS results not consistent
No systematic difference
Possible Explanations: different versions of Geant4, different physics packages, geometry or different technique of rejecting events.
Next Step : Compare pre filter/veto results e.g. number of detected gamma rays interacting via Compton scattering or theoretical values ( Compton edge)

## Slide 10: Results-662 keV
Chart: Incident gamma ray energy of 662 keV
| 100.0 | 300.0 | 750.0 | 1000.0
GAMOS | 206 | 810 | 2531 | 3495
GEANT4 | 82 | 357 | 1458 | 2257

## Slide 11: Results-364 keV
Chart: Incident gamma ray energy of 364 keV
| 100.0 | 300.0 | 750.0 | 1000.0
GAMOS | 483 | 1472 | 3693 | 4937
GEANT-4 | 175 | 881 | 2718 | 3467