EDOC210

CDOC210

EUROGAM DATA ACQUISITION SYSTEM

CHARISSA DATA ACQUISITION SYSTEM

Register Server implementation for CAMAC

Edition 1.01

April 1995

Nuclear Physics Support Group

Central Laboratory of the Research Councils

Daresbury Laboratory

CAMAC Register Server

The CAMAC register server is an implementation of the generalised Eurogam register server concept which contains register classes specific to the requirements of access to CAMAC hardware. For details of the general Eurogam Register Server the Eurogam documents EDOC024, EDOC034, EDOC087 and EDOC088 should be consulted.

Definitions

format of numbers

decimal		1234

hexadecimal		0x1234 or @1234

binary			%1011

All register values are text strings unless otherwise specified.

data word bit identification

Data word bit identification uses bit 15 (for 16 bit data words) as the most significant bit and bit 0 as the least significant bit. (This differs from standard CAMAC identification which labels the most significant bit as 16 and the least significant bit as 1.)

register names

Register names are text strings which may contain any printable character. No restrictions are placed on the form of a register name except that it must be meaningful to the specific server. The client may access multiple registers in a single request by the use of ‘wild card’ characters within the supplied name.

The use of ‘*’ within a name will cause a match with all defined registers which compare with the supplied name when the ‘*’ is replaced by any required string. For example the name this*register will match with the registers thisfirstregister and this1stregister. As a extreme (but very useful) case the name * will match with all defined registers.

The use of ‘?’ within a name will cause a match with all defined registers which compare with the supplied name when the ‘?’ is replaced by a single character. The name may contain several ‘?’s and each ‘?’ will be replaced by one character. For example the name this???register will match with the registers this1stregister and this2ndregister but not with the register thisfirstregister.

The use of [range,.....,range] within a name allows a number of alternative strings which may be tried when attempting a match with the defined registers.  range may be a single integer or single letter or a range of letters (expressed as letter-letter) or a range of integers (expressed as integer-integer). For example the pattern [5,10-12,a-d,19] matches with any of the set {5,10,11,12,a,b,c,d,19}, and the name module[1-2].reset will match with the registers module1.reset and module2.reset. The use of ‘*’ and ‘?’ within a range specification is permitted. For example the name module?.reset will match with the registers module1.reset, module3.reset, modulea.reset etc etc.

Initial register class

The CAMAC register server contains on startup an inbuilt set of registers. These inbuilt registers are intended primarily for test and debugging and applications using the CAMAC register server should normally define specific registers for the modules being used.

register	Camac.Address	access permitted - read and write

defines the camac hardware address (c,n);  the camac operation (a,f); and if appropiate the data width (w)

write register 	defines values for c,n,a,f & w

format		parameter1 [parameter2 [parameter3 .......] ]

parameters	-c	camac crate

-n	camac station

-a	operation subaddress

-f 	operation function

-w	data width (of camac access) (may be 16 or 24 bits)

example	-c 1   -n 16    -a 0    -f 0   -w 24

selected parameters may be defined or redefined

example	-n 18

read register	returns the current values of the parameters as a text string in the same format as a complete write register

Note - this register will aways return the values of c,n,a,f,& w used by the last CAMAC access and is thus useful as a diagnostic tool for debugging actions of defined specfic registers.

initialise register	set parameters to default values

(-c 1  -n 1  -a 0  -f 0  -w 16)

register	Camac.Execute	access permitted - read and write

executes a camac cycle using parameters currently defined via the camac.address register

write register	the data supplied is taken and a camac (write) cycle executed

read register	a camac (read) cycle is executed and the data obtained is returned

Note - for both register operations the value of the parameter f should be appropiate for the action (read or write) requested.

register	Camac.Status	access permitted - read only

holds q & x returned by the last camac operation

read register	returned data  %qx        ie  %11

Note - this register will always return the values of q and x returned by the last CAMAC access.

register	Camac.Data		access permitted - read only

holds data used by the last CAMAC operation - either supplied (write) or returned (read)

read register	returned data  0xabcd  (or 0xabcdef if 24 bit)

Note - this register will always return the data used by the last CAMAC access. Dataless CAMAC operations will not change its value.

register	Camac.Debug	access permitted - read and write

controls the server debug level

write register	set the server debug level

read register	return the server debug level

initialise register	set the server debug level to 0 (ie off)

Debugging messages are controlled by a set of bit flags which can be Ored  together to create a debug “level”. The following flags have been defined. If a flag bit is set then debug messages from the specified procedures will be produced.

0x01		interface card procedures (currently Hytec VSD2992)

0x02		intrinsic register procedures

0x04		xCAMAC class procedures

0x08		cCAMAC class procedures

0x10		qCAMAC class procedures

Configuration register class

When the register server task starts it creates a single instance of the configuration register class and initialises it using the name of the configuration file given when spawing the register server. The records of the configuration file have exactly the same form as the command line interface to the register server (see EDOC088) except that the -f and -c parameters are omitted and the data format is assumed to be a (ascii characters).

ie.	ersdefine	register-name	class-name

erswrite	register-name	data

eg.	ersdefine	fdt32#1.control	xCAMAC

erswta		fdt32#1.control	-c 1  -n 4  -a 0  -f 16  -w 16

-p wo  -I 0  -b 0  -i 0

erswrite	fdt32#1.control	0x9

These three lines would define a register fdt32#1.control and write the value 9 to it using the CAMAC operation f(16) a(0) to the module at c=1, n=4.

xCAMAC register class

The xCAMAC register class is used for all single shot CAMAC accesses. The register value is a data item of length (in bits) given by the -l attribute which occupies a field in the CAMAC data word with least significant bit given by the -b attribute. Whole words can be accessed by setting the length and bit attributes to zero. The class accepts data values in decimal, hexadecimal or binary format.

Register values for the xCAMAC class are text strings.

register attributes

-c	CAMAC crate address

-n	CAMAC station address

-a	CAMAC subaddress

-f	CAMAC function

-w	width of CAMAC data access (16,24 bits)

-p	access capability to CAMAC (rw, ro, wo)

-l	length of bit field

-b	bit position

-i	initial value

-z	data format (d (decimal), x (hexadecimal), b (binary))

-q	if = 1 return Q & X as a second data item for read-register

requests in the form %QX

default attributes :  -c 1  -n 1  -a 0  -f 0  -w 16  -p ro  -l 0  -b 0  -z x  -q 0

The default attribute value is used for any attribute not defined by a write-attributes command.

CAMAC function  -  convention determines if the operation is read or write.

f  le 7				read only

f  ge 16 and le 23		write only

f  ge 8 and le 15		invalid - use the cCAMAC class

f  ge 24			invalid - use the cCAMAC class

data format  -  data for write operations may be supplied in any format but the data format attribute will determine the format used when returning data from read operations.

For registers having access attribute rw the function attribute (f) defined is used for read-register operations and (f+16) is used for write-register operations.

The initialise-register operation is permitted only for registers having access attribute rw or wo and will only write data to CAMAC if an initial value has been explicitly defined with the -i attribute.

cCAMAC register class

The cCAMAC register class is used for all CAMAC accesses which do not require CAMAC data.

register attributes

-c	CAMAC crate address

-n	CAMAC station address

-a	CAMAC subaddress

-f	CAMAC function

-q	if = 1 return Q & X as a data item for read-register requests in

the form %QX

default attributes :  -c 1  -n 1  -a 0  -f 0  -q 1

The default attribute value is used for any attribute not defined by a write-attributes command.

CAMAC function  -  convention determines if the operation is dataless.

f  ge 8 and le 15		ok

f  ge 24			ok

f  le 7				invalid - use the xCAMAC class

f  ge 16 and le 23		invalid - use the xCAMAC class

The initialise-register function for this class is a no-operation.

qCAMAC register class

The qCAMAC register class is used for CAMAC accesses which require to read or write blocks of binary data using CAMAC Q repeat access mode. The data source (write to CAMAC) or destination (read from CAMAC) is a file.

register attributes

-c	CAMAC crate address

-n	CAMAC station address

-a	CAMAC subaddress

-f	CAMAC function

-w	width of CAMAC data access (16,24 bits)

-p	access capability to CAMAC (ro, wo)

-l	length of data block (words of -w bits)

-i	initial value

default attributes :  -c 1  -n 1  -a 0  -f 0  -w 16  -p ro  -l 0

The default attribute value is used for any attribute not defined by a write-attributes command.

CAMAC function  -  convention determines if the operation is read or write.

f  le 7				read only

f  ge 16 and le 23		write only

f  ge 8 and le 15		invalid - use the cCAMAC class

f  ge 24			invalid - use the cCAMAC class

The initialise-register operation is permitted only for registers having access attribute rw or wo and will only write data to CAMAC if an initial value has been explicitly defined with the -i attribute.

CAMAC write functions - The write-register operation supplies as data a text string which is the name of a file containing the data to be written to CAMAC.The data length written to CAMAC is defined by the minimum of the length requested by the -l attribute and the length of the data file. The data in the file is assumed to be in a raw bit-image format. It is expected to be big-endian (the most significant byte of each data word (16 or 24 bits) is read first). The initialise-register operation uses the -i attribute which is a text string as the name of the file to use. The data is written to CAMAC using the cnaf code defined. After each CAMAC write operation the Q bit is checked and the block transfer aborted if Q=0 (except that Q=0 is allowed for the last word of the block). The read-register operation performs no CAMAC accesses but returns the name of the file last used (or a null string) by a write operation.

CAMAC read functions - The write-register operation supplies as data a text string which is the name of a file to which data read from CAMAC should be written. The initialise-register operation uses the -i attribute which is a text string as the name of the file to use. The data is read from CAMAC using the cnaf code defined. After each CAMAC read operation the Q bit is checked and the block transfer aborted if Q=0 (except that Q=0 is allowed for the last word of the block). The read-register operation performs no CAMAC accesses but returns the name of the file last used (or a null string) by a write operation.