EDOC212

EUROGAM DATA ACQUISITION SYSTEM

Register Definitions for the LeCroy 4300B ADC

Edition 1.0

April 1995

Nuclear Physics Support Group

Central Laboratory of the Research Councils

Daresbury Laboratory

Registers for the LeCroy 4300B ADC module

This document should be read in conjunction with the document EDOC210 which describes the Register Server implementation for CAMAC.

This is a 16 channel ADC module with FERA and CAMAC data readout.

All register attributes include -c (crate address) and -n (station address)

Registers using the xCAMAC class of the CAMAC Register Server

status register 		read by f(0) a(0)  &  write by f(16) a(0)

The status register is composed of two distinct sections. The least significant 8 bits contain the Virtual Station Number (VSN) which determines the address of the data source during FERA readout. The most significant 8 bits determine the readout modes.

bit 8	EPS		ECL port Pedestal Subtraction: when EPS=1, 					pedestals are subtracted for ECL port readout

bit 9	ECE		ECL port data Compression Enable: when ECE=1, 				data zeros or zeros-and-overflows are suppressed 				for ECL port readout

bit 10	EEN		ECL port Enable: when EEN=1, ECL port readout 				is permitted

bit 11	CPS		CAMAC Pedestal Subtraction: when CPS=1, 					pedestals are subtracted for CAMAC readout

bit 12	CCE		CAMAC data Compression Enable: when CCE=1, 				data zeros or data zeros-and-overflows are 					suppressed for CAMAC sequential readout

bit 13	CSR		CAMAC Sequential Readout: when CSR=0, 					CAMAC random access readout is enabled; when 				CSR=1, CAMAC sequential readout is enabled

bit 14	CLE		CAMAC Lam Enable: when CLE=1, LAM is 					enabled

bit 15	OFS		OverFlow Suppression: when OFS=1, data 					readouts are suppressed during ECL port readout 				in conjunction with ECE=1 and for CAMAC 					sequential readout in conjunction with CCE=1

lc4300b#*.status		attributes  -a 0  -f 0  -w 16  -p rw  -l 0  -b 0  -z x -i 0

lc4300b#*.status.vsn	attributes  -a 0  -f 0  -w 16  -p rw  -l 8  -b 0  -z x

lc4300b#*.status.mode	attributes  -a 0  -f 0  -w 16  -p rw  -l 8  -b 8  -z x

lc4300b#*.status.eps	attributes  -a 0  -f 0  -w 16  -p rw  -l 1  -b 8  -z d

lc4300b#*.status.ece	attributes  -a 0  -f 0  -w 16  -p rw  -l 1  -b 9  -z d

lc4300b#*.status.een	attributes  -a 0  -f 0  -w 16  -p rw  -l 1  -b 10  -z d

lc4300b#*.status.cps	attributes  -a 0  -f 0  -w 16  -p rw  -l 1  -b 11  -z d

lc4300b#*.status.cce	attributes  -a 0  -f 0  -w 16  -p rw  -l 1  -b 12  -z d

lc4300b#*.status.csr	attributes  -a 0  -f 0  -w 16  -p rw  -l 1  -b 13  -z d

lc4300b#*.status.cle	attributes  -a 0  -f 0  -w 16  -p rw  -l 1  -b 14  -z d

lc4300b#*.status.ofs	attributes  -a 0  -f 0  -w 16  -p rw  -l 1  -b 15  -z d

Pedestal memory	read by f(1) a(x) and write by f(17) a(x)

The pedestal memory (8 bits) is accessed for channel x (0-15) using subaddress x.

lc4300b#*.adc*.pedestal	attributes  -a x  -f 1  -w 16  -p rw  -l 8  -b 0 -i 1

ADC data 			read by f(2) a(x)

random access or sequential readout of the 16 ADC values via the CAMAC dataway. Channel x (0-15) is selected using subaddress x in random access readout only (CSR=0). In sequential mode (CSR=1) the subaddress is ignored.

lc4300b#*.adc*.data	attributes  -a x  -f 2  -w 16  -p ro  -l 0  -b 0

Registers using the cCAMAC class of the CAMAC Register Server

These registers do not require data and have no initial value. However read-register operations may return Q and X as data.

reset				write or read by f(9) a(0)

module reset

lc4300b#*.reset		attributes  -a 0  -f 9

test LAM			read by f(8) a(0)

returns Q=1 if the module LAM is set

lc4300b#*.testlam		attributes  -a 0  -f 8

test LAM and clear	read by f(10) a(0)

returns Q=1 if the module LAM is set and clears the LAM

lc4300b#*.testclearlam	attributes  -a 0  -f 10

test module		read by f(25) a(0)

returns Q=1 if BUSY =0,  returns Q=0 if the module is not in the “ready” state.

lc4300b#*.test		attributes  -a 0  -f 25