EDOC215

CDOC215

CHARISSA DATA ACQUISITION SYSTEM

Register Definitions for the LeCroy 2375 module

Edition 1.0

April 1995

Nuclear Physics Support Group

Central Laboratory of the Research Councils

Daresbury Laboratory

Registers for the LeCroy 2375 Data Stack Module

This document should be read in conjunction with the document EDOC210 which describes the Register Server implementation for CAMAC.

This is a fast 256 x 16 memory with separate read and write ECL ports used for data readout from modules having FERA outputs.

All register attributes include -c (crate address) and -n (station address)

Registers using the xCAMAC class of the CAMAC Register Server

Memory Address Read Pointer (RP)	read by f(0) a(1) & write by f(16) a(1)

The 8bit internal Read Pointer is used to define the next offset for read access to the data stack memory.

DS.rp		attributes  -a 1  -f 0  -w 16  -p rw  -l 8  -b 0  -i 0  -z d -i 0

Memory Address Write Pointer (WP)	read by f(0) a(4) & write by f(16) a(4)

The 8bit internal Write Pointer is used to define the next offset for write access to the data stack memory.

DS.wp		attributes  -a 4  -f 0  -w 16  -p rw  -l 8  -b 0  -i 0  -z d -i 0

Memory Access		read by f(0) a(0) & write by f(16) a(0)

Read or write a 16-bit dataword from memory as addressed by the Read Pointer (RP) or the Write Pointer (WP) and increment the Read or Write Pointer.

DS.data	attributes  -a 0  -f 0  -w 16  -p rw  -l 0  -b 0  -z x

Registers using the cCAMAC class of the CAMAC Register Server

These registers do not require data and have no initial value. However read-register operations may return Q and X as data.

reset				write or read by f(9) a(0)

module reset

DS.reset		attributes  -a 0  -f 9