CDOC217

CHARISSA DATA ACQUISITION SYSTEM

Register Definitions for the Event Controller

Edition 1.0

April 1995

Nuclear Physics Support Group

Central Laboratory of the Research Councils

Daresbury Laboratory

Registers for the Charissa Event Control module

This document should be read in conjunction with the document EDOC210 which describes the Register Server implementation for CAMAC.

All register attributes include -c (crate address) and -n (station address)

Registers using the xCAMAC class of the CAMAC Register Server

control register 		write by f(17) a(2)

Only bits 11 to 15 are used. The control register bits enable action if set as follows

bits 1-10	unused	=0

bit 11			enable cache read error LAM

bit 12			enable Read and Store timeout error LAM

bit 13			enable FERA timeout error LAM

bit 14			enable Trigger timeout error LAM

bit 15			enable Operation - enter EMO state

EC.control			attributes  -a 2  -f 17  -w 16  -p wo  -l 0  -b 0  -i 0

EC.control.enable		attributes  -a 2  -f 17  -w 16  -p wo  -l 4  -b 11

EC.control.Cacheerr	attributes  -a 2  -f 17  -w 16  -p wo  -l 1  -b 11

EC.control.RSMerr		attributes  -a 2  -f 17  -w 16  -p wo  -l 1  -b 12

EC.control.FERAerr		attributes  -a 2  -f 17  -w 16  -p wo  -l 1  -b 13

EC.control.Trigerr		attributes  -a 2  -f 17  -w 16  -p wo  -l 1  -b 14

EC.control.EMO		attributes  -a 2  -f 17  -w 16  -p wo  -l 1  -b 15

Digital Discriminator		read by f(0) a(2) & write by f(16) a(2)

The digital threshold is written in an 8 bit register.

This register can only be accessed when the Event Controller is not in the Module Operation (EMO) state.

EC.dd			attributes  -a 2  -f 0  -w 16  -p rw  -l 8  -b 0  -i 4

The Event Control Module contains a total register and a fera register.

The total register defines the total number of bytes that should be transferred per event between the EC module and the trigger interface and also the number of bytes of hit pattern which should be sent to the RSM. The value actually written to the hardware register is 1 less than this number.It is thus the total number of data channels rounded up to a multiple of 8, divided by 8 and less 1.

The fera register is similar but defines just those bytes which are reserved for FERA devices. It is thus the total number of fera channels rounded up to a multiple of 8, divided by 8 and less 1.

Total limit & control status		read by f(1) a(1)

The current value of the total register is returned in the least significant 8 data bits and the control status is returned in the most significant 8 data bits.

The control status bits indicate status if set as follows

bit 8			Module not busy

bit 9			Delay Mode

bit 10			Accept All Data

bit 11			Channel Number incorrect for FERA read

bit 12			Timing Error in Read and Store cycle

bit 13			Timing Error in FERA cycle

bit 14			Timing Error in Trigger cycle

bit 15			Module Operation Enabled (EMO state)

EC.rd_total			attributes  -a 1  -f 1  -w 16  -p ro  -l 8  -b 0  -z d

EC.status			attributes  -a 1  -f 1  -w 16  -p ro  -l 8  -b 8  -z x

EC.status.bit8		attributes  -a 1  -f 1  -w 16  -p ro  -l 1  -b 8  -z d

EC.status.bit9		attributes  -a 1  -f 1  -w 16  -p ro  -l 1  -b 9  -z d

EC.status.bi10		attributes  -a 1  -f 1  -w 16  -p ro  -l 1  -b 10  -z d

EC.status.bit11		attributes  -a 1  -f 1  -w 16  -p ro  -l 1  -b 11  -z d

EC.status.bit12		attributes  -a 1  -f 1  -w 16  -p ro  -l 1  -b 12  -z d

EC.status.bit13		attributes  -a 1  -f 1  -w 16  -p ro  -l 1  -b 13  -z d

EC.status.bit14		attributes  -a 1  -f 1  -w 16  -p ro  -l 1  -b 14  -z d

EC.status.EMO		attributes  -a 1  -f 1  -w 16  -p ro  -l 1  -b 15  -z d

Cache limit & control status	read by f(1) a(2)

The current value of the fera register is returned in the least significant 8 data bits and the control status is returned in the most significant 8 data bits.

EC.rd_cache			attributes  -a 2  -f 1  -w 16  -p ro  -l 8  -b 0  -z d

Cache & Total limits			write by f(17) a(1)

The value of the fera register is written in the least significant 8 data bits and the value of the total register is written in the most significant 8 data bits.

This register can only be accessed when the Event Controller is not in the Module Operation (EMO) state.

EC.cache			attributes  -a 1  -f 17  -w 16  -p wo  -l 8  -b 0  -i 0

EC.total			attributes  -a 1  -f 17  -w 16  -p wo  -l 8  -b 8  -i 0

Registers using the cCAMAC class of the CAMAC Register Server

These registers do not require data and have no initial value. However read-register operations may return Q and X as data.

enable LAM		write or read by f(26) a(0)

enable module LAM

EC.enable			attributes  -a 0  -f 26

disable LAM		write or read by f(24) a(0)

disable module LAM

EC.disable			attributes  -a 0  -f 24

test LAM			read by f(8) a(0)

returns Q=1 if the module LAM is set

EC.testlam			attributes  -a 0  -f 8

test LAM and clear	read by f(10) a(0)

returns Q=1 if the module LAM is set and clears the LAM

EC.testclearlam		attributes  -a 0  -f 10

reset module		read by f(11) a(1)

Complete clear of module

This register can only be accessed when the Event Controller is not in the Module Operation (EMO) state.

EC.reset			attributes  -a 1  -f 11

clear error status	write or read by f(11) a(2)

Clear all the error status bits in the Control Status register only

EC.clear			attributes  -a 2  -f 11

test EMO state		read by f(27) a(1)

returns Q=1 if the module is in the Enable Module Operation (EMO) state.

EC.test_EMO			attributes  -a 1  -f 27

test TEST state		read by f(27) a(2)

returns Q=1 if the module is in the TEST state.

EC.test_TEST			attributes  -a 2  -f 27

Simulate STROBE	write or read by f(25) a(0)

Simulate a Strobe input.

This register can only be accessed when the Event Controller is not in the Module Operation (EMO) state.

EC.strobe			attributes  -a 0  -f 25